JCECE Entrance Exam Paper

Ques.1) Doubling the voltage gain causes a ________ dB ________.

10, increase

6, increase

10, decrease

6, decrease

Answer: 2

Ques2.)________ frequencies are values of frequency at which the RC circuits reduce the voltage gain to 70.7% of its midrange value.

Critical

Cutoff

Corner

all of the above

Answer: 4

Ques.3)A roll-off of 20 dB per decade is equivalent to a roll-off of ________ per octave.

3 dB

13 dB

12 dB

6 dB

Answer: 4

Ques.4) An amplifier has an Rin = 1.2 k. The coupling capacitor is 1 F. Determine the approximate lower cutoff frequency.

133 Hz

1.33 kHz

13.3 kHz

133 kHz

Answer: 1

Ques.5) According to principle of conservation of energy, the total momentum of a system of masses in any direction remains constant unless acted upon by an external force in that direction.

True

False

Answer: 2

Ques.6)The friction experienced by a body, when in motion, is known as

rolling friction

dynamic friction

limiting friction

static friction

Answer: 2

Ques.7) Two balls of equal mass and of perfectly elastic material are lying on the floor. One of the ball with velocity v is made to struck the second ball. Both the balls after impact will move with a velocity

v

v/2

v/4

v/8

Answer: 2

Ques.8) The term â€˜forceâ€™ may be defined as an agent which produces or tends to produce, destroys or tends to destroy motion.

Agree

Disagree

Answer: 1

Ques.9) The coefficient of restitution for elastic bodies is one.

Correct

Incorrect

Answer: 2

Ques.10) Strain energy is the

energy stored in a body when strained within elastic limits

energy stored in a body when strained upto the breaking of a specimen

maximum strain energy which can be stored in a body

proof resilience per unit volume of a material

Answer:1

Ques.11)A vertical column has two moments of inertia (i.e. Ixx and Iyy ). The column will tend to buckle in the direction of the

axis of load

perpendicular to the axis of load

maximum moment of inertia

minimum moment of inertia

Answer: 4

Ques.12) The neutral axis of the cross-section a beam is that axis at which the bending stress is

zero

minimum

maximum

infinity

Answer: 1

Ques.13) Eulerâ€™s formula holds good only for

short columns

long columns

both short and long columns

weak columns

Answer: 2

Ques.14) The object of caulking in a riveted joint is to make the joint

free from corrosion

stronger in tension

free from stresses

leak-proof

Answer: 4

Ques.15)Powder metallurgy process does not make metal powder by

atomisation

grinding/milling

hammering

electrolytic deposition

Answer: 3

Ques.16) In the blast furnace, incorporation of water vapour in the blast gives the following effect.

Increases the reducing potential of the gas.

Increases the flame temperature.

No significant change occurs.

Increases the hydrogen content in the metal.

Answer: 1

Ques.17) Pick out the wrong statement.

A ferromagnetic material becomes paramagnetic above the â€˜Curie temperatureâ€™.

Permanent magnets are made of hard materials, whereas electromagnets require soft magnetic materials.

Soft magnetic materials (e.g., pure iron) have higher permeability and low hysterisis loss and coercive forces

Tungsten steel and alnico are not hard magnetic materials.

Answer: 4

Ques.18) The usual energy consumption in electric arc furnace steel making is __________ KWh/ton of steel.

60 â€“ 100

400 â€“ 700

1200 -1500

2000 â€“ 2300

Answer: 2

Ques.19) Maximum permissible air velocity in pipelines is about __________ metre/second.

5

10

20

40

Answer: 2

Ques.20) A molecular technique in which DNA sequences between two oligonucleotide primers can be amplified is known as

southern blotting

northern blotting

polymerase chain reaction

DNA replication

Answer: 3